# Important Items To Remember

## Code sections

SPS 383.21 (1) (a) 1. a.

SPS 383	.21		(1)		(a)		2.		a.

Chapter

(ch.)

Section

(s.)

Subsection

(sub.)

Paragraph

(par.)

Subdivision

(subd.)

Subparagraph

(subpar.)

## Septic tank sizing for a 3-year service cycle

2.088 x Estimated Wastewater Flow x 1.5

## Velocity in a full pipe

Q/(2.448 x d2)			Where:		Q =  flow in gpm

d =  nominal inside diameter of pipe

## Ratio of the circumference of a circle to its diameter

pi (() = 3.14159

## Circumference of a circle

( x diameter

## Area of a circle

( x radius2

## Volume of a cylinder

( x radius2 x height

## Area of a rectangle

Length x width

## Volume of a cube

Length x width x depth

Weight of water per gallon

8.345 pounds

## Gallons per cubic foot

7.48

## Cubic inches per gallon

231

## Cubic inches per cubic foot

1728

## Cubic feet per cubic yard

27

## Percent (%) slope

(Height / Length) x 100

## Pressure

0.434 psi per foot of elevation

## Weight of concrete

Approximately 145 pounds per cubic foot

## Weight of water per cubic foot

62.43 pounds

## Weight of soil

Approximately 98 pounds per cubic foot

# Text boxes

MINIMUM FLOW RATE

TO MAINTAIN 2 FPS VELOCITY

1½” – 12 GPM

2” – 21 GPM

2½” – 30 GPM

3” – 46 GPM

±10% of shown pump curve for performance