SYSTEM SPECIFICATIONS

# In-ground Soil Absorption Component

Component Manual # ______________________________

# Project Name: _____________________________

## Distribution Cell Type

Aggregate       Non-Aggregate

Type of Non-Aggregate Component

_______________________________

Manufacturer____________________

Model__________________________

Number of Bedrooms		_______

Soil Application Rate (DLR)   ______ gpd/ft2

(Designed Loading Rate)

Wastewater Quality

Treated			Untreated

Combined wastewater:

Number of bedrooms		            _______

gal/day/bedroom					   x 150

Daily Wastewater Flow (DWF)   = _______

Clear and graywater only:

Number of bedrooms		    	      _______

gal/day/bedroom						x 90

Daily Wastewater Flow (DWF)   =  _______

Blackwater

Number of bedrooms		              _______

gal/day/bedroom					       x 60

Daily Wastewater Flow (DWF)   =    _______

Dispersal Area  (Aggregate)

______ ÷ ______= ______ ft2

(DWF)         (DLR)

Dispersal Area (Non-Aggregate)

EISA Rating  ______ft2

System sizing = DWF ÷ DLR ÷ EISA

(______ ÷ ______) ÷ ______= ______ chambers

(DWF)	      (DLR)           (EISA)

Diverter valve	yes	  	no

Manufacture	________________________

Septic Tank

Min. Septic Tank Vol. Req.		______ gal.

Septic Tank Volume			______ gal.

Manufacturer ______________________

## Effluent Filter

Manufacturer ______________________

Model ____________________________

Pump Tank

Manufacturer ______________________

Volume ___________________________

Model 	___________________________

Distribution Component

Distribution Box

Hydro-splitter

Other ___________________________

Manufacturer _____________________

Cross section of distribution cell(s)